## Slide 1: RF & Microwave Power Amplifier Design Preliminary Design Report
Name: Eric Valentino
Date: 2/27/19

## Slide 2: Design Project goals
Parameter | Assignment min. | Datasheet Max | Goal
P_out_max | 38 dBm | 40.4 dBm | 38 dBm
Maximum Efficiency | 60 % | 68.8 | 75%
Gain | N/A | 41.4 | 

## Slide 3: Summary of Design Approach & Procedures: Input Match
In order to evaluate the input match, we want to make sure we are trying to match to something that will be close to Γ_in*, and not S_11*.
  In order to get a better picture of what the Γ_in* would look like when the PA was appropriately matched, I decided to present the Z_l,opt at the extrinsic plane which was solved for in the stabilization exercise: 16.8 – j1.43
Γin for 50 Ω and 16- 1.4 Ω

## Slide 4: Re-Evaluating Stability
Looking back on stability exercise, it turned out dB(s21) of the stability network was around 6 dB at the design frequency
Went back and tuned to get
  Series R: 4.9 Ω
  Seriec C: 14.41 pF
  Shunt R: 113 Ω
  Shunt C : 100 pF
Unconditionally stable again, but instead with 1.8 dB of insertion loss at design frequency

## Slide 5: Initial Match
Now input match was assessed.
The input matching network, transistor with Zl = Zl,opt, and input matching network connected to transistor with Zl = Zlopt were all simulated in order to generate plots shown
R_in about 5 ohms, but low Q at design frequency
Decided to employ Vendelin matching

## Slide 6: Input Match Design
Original
Addition of Mlin
Addition of stubs
Markers now at 2.1 and 4.1 GHz
Tuning Stub Lengths
Don’t want to directly use quarter wave transformer because Q will be high, so will use series of high impedance transmission line sections and shunt capacitors to reach 50 Ω while staying below a Q of 1 which the gate impedance started at.
One option two quarter wave transformers
9 Ω then 35 Ω

## Slide 7: Input Match Design
Another option: Series T-lines and capacitors
L1: Z0 = 30Ω , 7.1°
C1: 6.8 pF
L2: Z0 = 35Ω, 13.5°
C2: 3.01 pF
L3: Z0 = 50Ω, 30.1 °
C3: 1.2 pF
Ended up getting excellent match with about 1.1 GHz BW:

## Slide 8: Output Matching Design

## Slide 9: Best Effort Results
Show |S11|, |S21|, |S22| vs. freq. (same graph)
Gain , Pout & PAE vs. Pin (may be able to use 1 graph) at center frequency.
Gain , Pout & PAE at design bandwidth edges.

## Slide 10: Best Effort Schematic
Show input & output matching networks in as much detail as you can on 1 or 2 slides max.

## Slide 11: Best Effort Layout
Make sure you show estimated outer dimensions.

## Slide 12: List of Materials/Components Needed
Be as complete as possible in terms of components, connectors and other materials you may need.

## Slide 13: Summary of Design Readiness And Remaining Issues or Steps
How close are you to “submitting to fabrication”?